The driver for the rtl 8191cu wireless usb adapter had to be downloaded from the maunfacturer's website.

Per the driver's documentation, the driver source tar ball needs to be decompressed.

tar zxvf rtl8188C_8192C_usb_linux_v4.0.2_9000.20130911tar.gz

The Makefile then needs to be edited.

Since the processor used on the RPi is not listedwe must add it. Following the list of processor platforms, we add a new platform:

CONFIG_PLATFORM_ARM_1176JZFS = y

Then we create a corresponding entry inside the platform setting section:

ifeq ($(CONFIG_PLATFORM_ARM_1176JZFS),y)
EXTRA_CFLAG+= -DCONFIG_LITTLE_ENDIAN
ARCH:= arm
CROSS_COMPILE:=
KSRC:= /lib/modules/3.6.11+/modules.builtin
MODDESTDIR:= /lib/modules/3.6.11+/kernel/drivers/net/wireless/
MODULE_NAME:= wlan
endif

The driver folder must now be moved (from the location of unzipping and decompression) to the kernel, specifically to a new folder named: /lib/modules/3.6.11+/kernel/drivers/net/wireless/rtl8192cu

Within file:
/lib/modules/3.6.11+/kernel/drivers/net
/wireless/rtl8192cu/includes/autoconf.h
 at the end of the initial #define list, we add
#define CONFIG_LITTLE_ENDIAN 1

Create a new file :
/lib/modules/3.6.11+/kernel/drivers/net/wireless/Kconfig
containing the line:
source “/lib/modules/3.6.11+/kernel/drivers/net/wireless/rtl8192cu/Kconfig”

We then append the Makefile with:
obj-$(CONFIG_RTL8192CU) += rtl8192cu/

Download a new, “clean” kernel source tree to usr/src/linux-rpi-3.6.y.tar.gz, then extract it:
sudo tar -xzf usr/src/linux-rpi-3.6.y.tar.gz
(Be prepared for a rather lengthy extraction)

Once it is extracted, we link the new files with the existing kernel:
ln -s /usr/src/linux-rpi-3.6.y /lib/modules/3.6.11+/build
ln -s /usr/src/linux-rpi-3.6.y /lib/modules/3.6.11+/src
And include the current kernel config:
cp /proc/config.gz /usr/src/linux-rpi-3.6.y
cd /usr/src/linux-rpi-3.6.y
gunzip config.gz
mv config .config

make oldconfig && make prepare

Install isc-dhcp-server using apt

Edit the dhcpd.conf file located at /etc/dhcp/dhcpd.conf:
option domain-name “your_domain.your_lan”;
(where “your_domain” and “your_lan” are your chosen names, ie “Dude_the_Cat.net”)
option domain-name-server 209.18.47.61, 8.8.8.8, 8.8.4.4;
(using either the address of your DNS Server from your ISP or using a public DNS	server(s).)
subnet 192.168.3.0 netmask 255.255.255.0{
range 192.168.3.1 192.168.3.20;
option routers 68.172.218.115;
}
(The subnet value will be the LAN (Local Area Network) IP address for the router.)
(The range will be the available addresses for machines connected to the LAN)
(The “option routers” address is the WAN (Wide Area Network) IP address assigned by	the ISP)
host RPi_Router{
hardware ethernet b8:27:eb:df:d1:ea;
fixed-address 192.168.3.0;
}
(Where “RPi_Router is a chosen name, and the value b8:27:eb:df:d1:ea is the MAC	address of the raspberry pi)

Save the revised file.

To run the server:
service isc-dhcpd—server start
To stop the server:
service isc-dhcpd-server stop

Bibliography

Realtek 8192cu driver from http://www.realtek.com.tw/downloads/
[accessed on 11/1/2013]
- isc-dhcp-server from apt
- Kernel source tree for linux 3.6.11 http://raspberrypi.stackexchange.com/questions/5230/getting-no-rule-to-make-target-modules-stop-error-when-running-makefile-w
[accessed on 11/3/2013]